Copyright 2019 by The American Institute of Architects (AIA)

Exclusively published and distributed by Deltek, Inc. for the AIA

Revise this Section by deleting and inserting text to meet Project-specific requirements.

This Section uses the term "Architect." Change this term to match that used to identify the design professional as defined in the General and Supplementary Conditions.

Verify that Section titles referenced in this Section are correct for this Project's Specifications; Section titles may have changed.

GENERAL

SUMMARY

Section Includes:

MCM interior wall or ceiling paneling.

Related Sections:

Retain subparagraphs below to cross-reference requirements Contractor might expect to find in this Section but are specified in other Sections.

Section 074213.23 "Metal Composite Material Wall Panels" for exterior metal-faced composite wall panels.

DEFINITIONS

MCM: Metal composite material; cladding material formed by joining two thin metal skins to polyethylene or fire-retardant core and bonded under precise temperature, pressure, and tension.

COORDINATION

Coordinate layout and installation of metal interior wall paneling with adjacent construction.

PREINSTALLATION MEETINGS

Retain "Preinstallation Conference" Paragraph below if Work of this Section is extensive or complex enough to justify a conference.

Preinstallation Conference: Conduct conference at [Project site] <Insert location>.

ACTION SUBMITTALS

Action submittals are submittals requiring responsive action and return of reviewed documents to Contractor.

Product Data: For each type of product.

Include construction details, material descriptions, dimensions of individual components and profiles, and finishes for each type of panel and accessory.

Sustainable Design Submittals:

Sustainability Submittals:

For 3A Composites' "SUSTAINABILITY" information, see https://alucobond.com/products/sustainability.

Retain "Environmental Product Declaration (EPD)," "Health Product Declaration (HPD)" and "Sourcing of Raw Materials" subparagraphs below to be eligible for LEED v4 credit. See the Evaluations.

"Environmental Product Declaration (EPD)" Subparagraph below applies to LEED v4 (all) MR Credit, "Building Product Disclosure and Optimization - Environmental Product Declarations." Verify, with manufacturer, that EPDs are available for each product.

Shop Drawings:

Include fabrication and installation layouts of MCM panels; details of edge conditions, joints, panel profiles, corners, anchorages, attachment system, trim, flashings, closures, and accessories; and special details.

Accessories: Include details of the flashing, trim, and anchorage systems, at a scale of not less than 1-1/2 inches per 12 inches (1:10).

Retain "Samples for Initial Selection" and "Samples for Verification" paragraphs below for two-stage Samples.

Samples for Initial Selection: For each type of MCM panel indicated with factory-applied finishes.

Include Samples of trim and accessories involving color selection.

Samples for Verification: For each type of exposed finish, prepared on Samples of size indicated below:

MCM Panels: 12 inches (305 mm) long by actual panel width. Include fasteners, closures, and other MCM panel accessories. Submit custom color samples in paint manufacturer's standard size.

INFORMATIONAL SUBMITTALS

Informational submittals are submittals that require review by Architect, but they do not require Architect's responsive action and return of reviewed documents to Contractor, provided submittals comply with requirements. If rejected, submittals with responsive action must be returned to Contractor.

Coordinate "Qualification Data" Paragraph below with qualification requirements in Section 014000 "Quality Requirements" and as may be supplemented in "Quality Assurance" Article.

Qualification Data: For Installer.

Product Test Reports: For each product, for tests performed by a qualified testing agency.

CLOSEOUT SUBMITTALS

Maintenance Data: For MCM panels to include in maintenance manuals.

MAINTENANCE MATERIAL SUBMITTALS

See Section 017700 "Closeout Procedures" for submission of maintenance material items.

Extra Stock Material: Furnish extra materials[, from the same production run,] to Owner that match products installed and that are packaged with protective covering for storage and identified with labels describing contents.

Revise "Metal Interior Wall Paneling Components" Subparagraph below to suit Project. If preferred, replace percentage with a specific number of metal panels and pieces of each component and their lengths.

Metal Interior Wall Paneling Components: Quantity of each metal wall panel unit and accessory equal to [2] <Insert number> percent of quantity installed.

Mockups

When necessary, build mockups to verify selections made under Sample submittals and to demonstrate aesthetic effects and set quality standards for fabrication and installation.

Retain first subparagraph below for large-scale mockup. Indicate portion of building represented by mockup on Drawings or draw mockup as separate element. Revise to suit Project or if larger mockup is needed for field performance testing.

Build mockup of typical MCM panel assembly [as shown on Drawings] <Insert size>, including [corner,] [soffits,] supports, attachments, and accessories.

Approval of mockups does not constitute approval of deviations from the Contract Documents contained in mockups unless Architect specifically approves such deviations in writing.

Retain subparagraph below if the intention is to make an exception to the default requirement in Section 014000 "Quality Requirements" for demolishing and removing mockups.

Subject to compliance with requirements, approved mockups may become part of the completed Work if undisturbed at time of Substantial Completion.

DELIVERY, STORAGE, AND HANDLING

Deliver components, MCM panels, and other manufactured items to Project site in original, unopened packages and store them in a fully enclosed, conditioned space where they are protected against damage from moisture, humidity, temperature extremes, direct sunlight, surface contamination, and other causes. Package MCM panels for protection during transportation and handling.

Unload, store, and erect MCM panels, components, and accessories in a manner to prevent bending, warping, twisting, and surface damage.

Stack MCM panels horizontally on platforms or pallets, covered with suitable weathertight and ventilated covering. Store MCM panels to ensure dryness, with positive slope for drainage of water. Do not store MCM panels in contact with other materials that might cause staining, denting, or other surface damage.

Retain strippable protective covering on MCM panels during installation.

FIELD CONDITIONS

Environmental Limitations: Do not install metal interior wall paneling until spaces are enclosed and weathertight, wet-work in spaces is complete and dry, and HVAC system is operating and maintaining temperature and relative humidity at levels planned for building occupants during the remainder of the construction period.

WARRANTY

When warranties are required, verify with Owner's counsel that special warranties stated in this article are not less than remedies available to Owner under prevailing local laws.

Special Warranty: Manufacturer's standard form in which manufacturer agrees to repair or replace MCM panels that fail in materials within specified warranty period.

Failures include, but are not limited to, the following:

Structural failures including rupturing, cracking, or puncturing.

Deterioration of metals and other materials beyond normal weathering.

Verify available warranties and warranty periods for MCM panels.

Warranty Period: [ten] years from date of Substantial Completion.

Special Warranty: Installer’s workmanship warranty in which fabricator and/or installer agrees to repair or replace MCM panels that fail in materials within specified warranty period.

Failures include, but are not limited to, the following:

Structural failures including rupturing, cracking, or puncturing.

Deterioration of metals and other materials beyond normal weathering.

Verify available warranties and warranty periods for MCM panels.

Warranty Period: [two] years from date of Substantial Completion

Special Warranty on Panel Finishes: Manufacturer's standard form in which manufacturer agrees to repair finish or replace MCM panels that show evidence of deterioration of factory-applied finishes within specified warranty period.

Retain "Exposed Panel Finish" Subparagraph below for fluoropolymer finishes; verify availability with manufacturer.

Exposed Panel Finish: Deterioration includes, but is not limited to, the following:

Color fading more than 5 Delta E units when tested according to ASTM D2244.

Chalking in excess of a No. 8 rating when tested according to ASTM D4214.

Cracking, checking, peeling, or failure of paint to adhere to bare metal.

Verify available warranties for MCM panel finishes and insert number in "Finish Warranty Period" Subparagraph below. A 20-year period is available for fluoropolymer finish and is the maximum included with manufacturers' published data; a 10-year period is usually available for siliconized polyester. Longer periods for premium finishes may be available.

Finish Warranty Period: [20] [10] <Insert number> years from date of Substantial Completion.

PRODUCTS

Manufacturers and products listed in this Section are neither recommended nor endorsed by the AIA or Deltek. Before selecting manufacturers and products, verify availability, suitability for intended applications, and compliance with minimum performance requirements. For definitions of terms and requirements for Contractor's product selection, see Section 016000 "Product Requirements."

Product options commonly available from manufacturers are included in square brackets throughout the Section Text. Not every manufacturer listed can provide every option offered; verify availability with manufacturers. For definitions of terms and requirements for Contractor's product selection, see Section 016000 "Product Requirements."

Source Limitations

Retain this article to limit sources for the entire Section. Source limitations may also be specified in individual articles if desired.

    - Obtain components and materials specified in this Section from manufacturers with third party quality inspection programs.

PERFORMANCE REQUIREMENTS

    - Structural Performance: Metal interior wall paneling to withstand the effects of gravity loads and the following loads and stresses within limits and under conditions indicated without permanent deformation of components, noise, or metal fatigue caused by rattle or flutter, or permanent damage to fasteners and anchors.

    - Surface-Burning Characteristics: For metal interior wall paneling, determined by testing in accordance with ASTM E84 by a qualified testing agency. Identify products with appropriate markings of applicable testing agency.

Flame-Spread Index: [25] <Insert value> or less.

Smoke-Developed Index: [100] <Insert value> or less.

Retain one of two "Seismic Performance" paragraphs below for projects requiring seismic design. Delete both if performance requirements are indicated on Drawings. Model building codes and ASCE/SEI 7 establish criteria for buildings subject to earthquake motions. Coordinate requirements with structural engineer.

    - Seismic Performance: As indicated on Drawings.

    - Seismic Performance: Metal interior wall paneling, including attachments to other construction, to withstand the effects of earthquake motions determined in accordance with [ASCE/SEI 7] <Insert requirement>.

Design earthquake spectral response acceleration, short period (Sds) is determined by Project's location and site classification. This information is usually provided in structural notes on Drawings.

      - Design earthquake spectral response acceleration, short period (Sds) for Project is <Insert value>.

Component Importance Factor is generally 1.0 unless the structure is in Seismic Use Group III, in which case the Component Importance Factor is 1.5.

      - Component Importance Factor: [1.5] [1.0].

METAL INTERIOR WALL PANELING

Retain "Basis-of-Design Product" Paragraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

    - Basis-of-Design Product: Subject to compliance with requirements, provide 3A Composites USA Inc.; ALUCOBOND PLUS or comparable product by one of the following:

Arconic Architectural Products (USA).

      - Mitsubishi Chemical Composites.

      - <Insert manufacturer's name>.

Wall Panels <Insert drawing designation>: Formed with 0.020-inch- (0.50-mm-) thick, [coil-coated] [anodized] aluminum sheet facings with manufacturer's standard fire-retardant core.

Panel Thickness: [0.157 inch (4 mm)] [As indicated on Drawings].

Finish: [PVDF fluoropolymer] [FEVE fluoropolymer] [Siliconized polyester] [Anodized] with coats and thicknesses that comply with MCM panel manufacturer's performance and warranty requirements.

For 3A Composites' "ALUCOBOND PLUS" standard stock colors, see https://d371dyuip757b1.cloudfront.net/downloads/StockColorChartJUNE2019.pdf.

For "ALUCOBOND PLUS" custom colors, see https://d371dyuip757b1.cloudfront.net/downloads/InspirationalChartJUNE2019.pdf.

For "METALLIC" colors, see https://alucobond.com/colours-surfaces/metallic.

For "naturAL TERRA SERIES" textured colors, see https://d371dyuip757b1.cloudfront.net/downloads/Alucobond_naturAL_TERRA_FEB-2018-download.pdf.

For more "Colours & Surfaces" selections, see https://alucobond.com/colours-surfaces.

            - Color: [As indicated by manufacturer's designations] [As selected by Architect from manufacturer's full range] [As indicated on drawing schedule].

When colors are selected, insert color in subparagraphs below to suit Project.

Color 1: <Insert color>.

Color 2: <Insert color>.

Color 3: <Insert color>.

Color 4: <Insert color>.

Peel Strength: 22.5 in-lb/in. (100 N x mm/mm) when tested for bond integrity in accordance with ASTM D1781.

MISCELLANEOUS MATERIALS

Miscellaneous Metal Sub-framing and Furring: ASTM C645, cold-formed, metallic-coated steel sheet, ASTM A653/A653M, G90 (Z275 hot-dip galvanized) coating designation or ASTM A792/A792M, Class AZ50 (Class AZM150) aluminum-zinc-alloy coating designation unless otherwise indicated. Provide MCM panel manufacturer's standard sections as required for support and alignment of metal interior wall paneling.

Joint Sealer, Interior: Non-sag, paintable, non-staining, latex sealant complying with ASTM C834; of type and grade required to seal joints in decorative formed metal; as recommended in writing by decorative formed metal manufacturer and with a VOC content of not more than 250 g/L when calculated according to 40 CFR 59, Subpart D (EPA Method 24).AA. Joint Sealer: Clear silicone sealant approved by MCM sheet manufacturer.

Retain panel accessories, flashing, and trim as required and coordinate with those specified in Section 076200 "Sheet Metal Flashing and Trim."

Panel Accessories: Provide components required for a complete metal interior wall panel system including trim, copings, fasciae, mullions, sills, corner units, clips, flashings, sealants, gaskets, fillers, closure strips, and similar items to provide finished appearance. Match material and finish of MCM panels unless otherwise indicated.

Backing Plates: Provide metal backing plates at panel end splices, fabricated from material recommended by MCM panel manufacturer.

Provide aluminum flashing such as ALUCOBOND AXCENT for closure conditions.

Fasteners: Manufacturer's standard. Use types and sizes to suit unit installation conditions.

First option in first subparagraph below specifies flush heads; second option specifies raised heads.

Use [Phillips flat-head] [hex-head or Phillips pan-head] [tamper-resistant] screws for exposed fasteners unless otherwise indicated.

For fastening aluminum, use aluminum fasteners or 300 series stainless steel fasteners.

For fastening galvanized steel, use hot-dip-galvanized-steel fasteners or 300 series stainless steel fasteners.

For exposed fasteners within color-finished metal interior wall paneling, use fasteners with heads that match color of panels.

FABRICATION

Fabricate and finish MCM panels and accessories at the factory, by MCM panel manufacturer's standard procedures and processes, as necessary to meet specified performance requirements. Comply with indicated profiles and with dimensional and structural requirements.

Sheet Metal Flashing and Trim: Fabricate flashing and trim to comply with MCM panel manufacturer's written instructions that apply to design, dimensions, metal, and other characteristics of item indicated.

Form exposed sheet metal accessories that are without excessive oil canning, buckling, and tool marks and that are true to line and levels indicated, with exposed edges folded back to form hems.

Fabricate nonmoving seams with flat-lock seams. Form seams and seal with epoxy seam sealer. Rivet joints for additional strength.

Conceal fasteners where possible. Exposed fasteners are not allowed on faces of accessories exposed to view.

Fabricate cleats and attachment devices from same material as accessory being anchored or from compatible, noncorrosive metal recommended in writing by MCM panel manufacturer.

Size: As recommended by SMACNA's "Architectural Sheet Metal Manual" or MCM wall panel manufacturer for application but not less than thickness of metal being secured.

FINISHES

Protect mechanical and painted finishes on exposed surfaces from damage by applying a strippable, temporary protective covering before shipping.

Appearance of Finished Work: Variations in appearance of abutting or adjacent pieces are acceptable if they are within one-half of the range of approved Samples. Noticeable variations in same piece are not acceptable. Variations in appearance of other components are acceptable if they are within the range of approved Samples and are assembled or installed to minimize contrast.

MCM Wall Panels:

Retain one fluoropolymer, siliconized-polyester, or anodized finish from subparagraphs below. Verify availability of finishes for products specified. If retaining more than one, indicate location of each on Drawings or by inserts. To obtain a proprietary finish system, insert names of coating manufacturers and products.

Revise or insert additional testing requirements in five fluoropolymer subparagraphs below if performance levels indicated in AAMA 2605 are insufficient.

Two-Coat Fluoropolymer: AAMA 2605. Fluoropolymer finish containing not less than 70 percent polyvinylidene fluoride (PVDF resin by weight in color coat. Prepare, pretreat, and apply coating to exposed metal surfaces to comply with coating and resin manufacturers' written instructions[ for seacoast and severe environments].

Three-Coat Fluoropolymer: AAMA 2605. Fluoropolymer finish containing not less than 70 percent polyvinylidene fluoride (PVDF) resin by weight in both color coat and clear topcoat. Prepare, pretreat, and apply coating to exposed metal surfaces to comply with coating and resin manufacturers' written instructions[ for seacoast and severe environments].

Mica Fluoropolymer: AAMA 2605. Two-coat fluoropolymer finish with suspended mica flakes containing not less than 70 percent polyvinylidene fluoride (PVDF) resin by weight in color coat. Prepare, pretreat, and apply coating to exposed metal surfaces to comply with coating and resin manufacturers' written instructions[ for seacoast and severe environments].

Metallic Fluoropolymer: AAMA 2605. Three-coat fluoropolymer finish with suspended metallic flakes containing not less than 70 percent polyvinylidene fluoride (PVDF) resin by weight in both color coat and clear topcoat. Prepare, pretreat, and apply coating to exposed metal surfaces to comply with coating and resin manufacturers' written instructions[ for seacoast and severe environments].

FEVE Fluoropolymer: AAMA 2605. Two-coat fluoropolymer finish containing 100 percent fluorinated ethylene vinyl ether (FEVE) resin in color coat. Prepare, pretreat, and apply coating to exposed metal surfaces to comply with coating and resin manufacturers' written instructions[ for seacoast and severe environments].

Siliconized Polyester: Epoxy primer and silicone-modified, polyester-enamel topcoat; with a dry film thickness of not less than 0.2 mil (0.005 mm) for primer and 0.8 mil (0.02 mm) for topcoat.

Exposed Anodized Finish:

Retain one of two options in "Clear Anodic Finish" Subparagraph below. Class I finish is heavy anodized. Verify availability with manufacturers.

Clear Anodic Finish: AAMA 611, [AA-M12C22A41, Class I, 0.018 mm] [AA-M12C22A31, Class II, 0.010 mm] or thicker.

Retain one of two options in "Color Anodic Finish" Subparagraph below. Verify availability with manufacturers.

Color Anodic Finish: AAMA 611, [AA-M12C22A42/A44, Class I, 0.018 mm] [AA-M12C22A32/A34, Class II, 0.010 mm] or thicker.

EXECUTION

EXAMINATION

Examine substrates, areas, and conditions, with Installer present, for compliance with requirements for installation tolerances, MCM panel supports, and other conditions affecting performance of the Work.

Examine roughing-in for components and systems penetrating MCM panels to verify actual locations of penetrations relative to seam locations of MCM panels before installation.

Proceed with installation only after unsatisfactory conditions have been corrected.

PREPARATION

Miscellaneous Supports: Install sub-framing, furring, and other miscellaneous panel support members and anchorages in accordance with MCM panel manufacturer's written instructions and approved Shop Drawings.

INSTALLATION

Install metal interior wall paneling in accordance with approved Shop drawings and manufacturer's written instructions in orientation, sizes, and locations indicated. Install panels perpendicular to supports unless otherwise indicated. Anchor MCM panels and other components of the Work securely in place.

Shim or otherwise plumb substrates receiving MCM panels.

Locate panel splices over, but not attached to, structural supports. Stagger panel splices and end laps to avoid a four-panel lap splice condition.

Align bottoms of MCM panels and fasten with blind rivets, bolts, or self-tapping screws. Fasten flashings and trim around openings and similar elements with self-tapping screws.

Metal Protection: Where dissimilar metals contact each other or corrosive substrates, protect against galvanic action as recommended in writing by MCM panel manufacturer.

Accessory Installation: Install accessories with positive anchorage to building as required for a complete MCM panel system; including trim, copings, corners, seam covers, flashings, fillers, closure strips, and similar items to provide finished appearance. Coordinate installation with flashings and other components.

Flashing and Trim: Comply with performance requirements and MCM panel manufacturer's written installation instructions. Provide concealed fasteners where possible, and set units true to line and level as indicated.

Install exposed flashing and trim that is without buckling and tool marks, and that is true to line and levels indicated, with exposed edges folded back to form hems. Install sheet metal flashing and trim to fit substrates and achieve specified performance.

Installer Qualifications: Company specializing in performing work of the type specified in this section.

With minimum <<3 years; or _____>> of<< documented; or None - N/A>> experience.

Submit contact names and phone numbers for at least <<three; or ____>> references connected with successful past projects.

CLEANING AND PROTECTION

Remove temporary protective coverings and strippable films, if any, as MCM panels are installed, unless otherwise indicated in manufacturer's written installation instructions. On completion of MCM panel installation, clean finished surfaces as recommended in writing by MCM panel manufacturer. Maintain in a clean condition during construction.

Remove and replace components that cannot be successfully cleaned and repaired to permanently eliminate evidence of damage, including dented and bent units.

END OF SECTION 097813